## Slide 1: Let’s Learn FreeCAD
Topic 3
3D Model

## Slide 2
Course Content
Introduction
Assembly
Create 3D Model
Topic 3
3D Model
Topic 3 has three subtopics including
Introduction, Create 3D Model & Assembly.
Topic 3

## Slide 3
Course Content
Introduction
Assembly
Create 3D Model
3D Model.
In FreeCAD, the Part Design Workbench is the perfect tool to build 3D model or part/product design.
Topic 3

## Slide 4
Course Content
Introduction
Assembly
Create 3D Model
Create 3D Model 1: Keychain.
The steps to create 3D Model as shown in figure below as follows:
Topic 3

## Slide 5
Course Content
Introduction
Assembly
Create 3D Model
The steps are:
Create new file and select Part Design Workbench .
Select create body, sketch, plane and Polyline.
Create freehand sketch. The Sketch might be like the figure below.
Topic 3

## Slide 6
Course Content
Introduction
Assembly
Create 3D Model
d. Select the appropriate constraint if necessary. The
constraint starts with the lines without constraint symbol.
e. For (d.), use Constraint vertically and Horizontally till the
constraint symbol appear.
Topic 3

## Slide 7
Course Content
Introduction
Assembly
Create 3D Model
f. Refer the drawing and use suitable constraint such as
Horizontally and Vertically distance, Diameter/Radius until
the sketch fully constraint.
Topic 3

## Slide 8
Course Content
Introduction
Assembly
Create 3D Model
g. Select circle and create circle with diameter of 16mm and
5mm.
h. Select Leave sketch . The view changed from 2D to
3D automatically.
i. Select Pad , insert length = 3mm and click ok.
j. Save file as: Key Chain
Topic 3

## Slide 9
Course Content
Introduction
Assembly
Create 3D Model
New File
To create the new file following steps:
1. Select a Create New
Topic 3

## Slide 10
Course Content
Introduction
Assembly
Create 3D Model
2. Select Workbench: Pull down -> Part Design
3. Window for Part Design workbench as follow:
Topic 3

## Slide 11
Course Content
Introduction
Assembly
Create 3D Model
New Sketch
The new sketch can be created using the steps below:
1. Select a Create Body on Combo view.
Topic 3

## Slide 12
Course Content
Introduction
Assembly
Create 3D Model
2. Select a Create Sketch.
3. Select a XY-Plane
Topic 3

## Slide 13
Course Content
Introduction
Assembly
Create 3D Model
4. Click Ok and the window as follow:
Topic 3