## Slide 1
The Introduction of DC Drives
Presented by : Fadzilah, Nor Hasrimin, Hamidah Haneym and Shahida

## Slide 2
  our team
FADZILAH HASHIM
SHAHIDA YUSOF
NOR HASRIMIN MD NOR
HAMIDAH HANEYM
AB HAMID

## Slide 3
•AN ELECTRICAL DRIVES CAN BE DEFINED AS AN ELECTROMECHANICAL DEVICE FOR CONVERTING ELECTRICAL ENERGY INTO MECHANICAL ENERGY TO IMPART MOTION TO DIFFERENT MACHINES AND MECHANISMS FOR VARIOUS KINDS OF PROCESS CONTROL.
•IT’S FUNCTIONS IS TO TURN AND DRIVE THE MOTOR ACCORDING TO LOAD REQUIREMENTS WITH RESPECT TO THE DESIRED TORQUE OR SPEED NEEDED BY THE USER.
DEFINITION OF ELECTRICAL DRIVES

## Slide 4
SPEED CONTROL METHODS OF DC SEPARATELY EXCITED MOTORS
The speed control by adding armature resistance
The speed control by adjusting armature voltage
The speed control by adjusting field voltage

## Slide 5
The operation
CONTROLLING SPEED BY ADDING RESISTANCE
Method 1:

## Slide 6
CONTROLLING SPEED BY ADDING RESISTANCE
A SETUP FOR SPEED CHANGE BY
ADDING AN ARMATURE RESISTANCE
EFFECT OF ADDING AN ARMATURE RESISTANCE ON SPEED

## Slide 7
CONTROLLING SPEED BY ADDING RESISTANCE
•ASSUME THAT THE FIELD AND ARMATURE VOLTAGES ARE CONSTANT.
•AT POINT 1, NO EXTERNAL RESISTANCE IS IN THE ARMATURE CIRCUIT.
•IF A RESISTANCE R_ADD1 IS ADDED TO THE ARMATURE CIRCUIT, THE MOTOR OPERATES AT POINT 2, WHERE THE MOTOR SPEED Ω_2
EFFECT OF ADDING AN ARMATURE RESISTANCE ON SPEED
EXPLANATION

## Slide 8
CONTROLLING SPEED BY ADDING RESISTANCE
EFFECT OF ADDING AN ARMATURE RESISTANCE ON SPEED
•IF THE ADDED RESISTANCE KEEPS INCREASING, THE MOTOR SPEED DECREASES UNTIL THE SYSTEM OPERATES AT POINT 4, WHERE THE SPEED OF THE MOTOR IS ZERO.
•THE OPERATION OF THE DRIVE SYSTEM AT POINT 4 IS KNOWN AS "HOLDING."
•IT IS QUITE COMMON TO OPERATE THE MOTOR UNDER ELECTRICAL HOLDING CONDITIONS IN APPLICATIONS SUCH AS ROBOTICS AND ACTUATION.
EXPLANATION

## Slide 9
CONTROLLING SPEED BY ADDING RESISTANCE
EFFECT OF ADDING AN ARMATURE RESISTANCE ON SPEED
...
EQUATIONS

## Slide 10
The operation
CONTROLLING SPEED BY ADJUSTING ARMATURE VOLTAGE
Method 1:

## Slide 11
CONTROLLING SPEED BY ADJUSTING ARMATURE VOLTAGE
A SETUP FOR SPEED CHANGE BY
ADJUSTING ARMATURE VOLTAGE
EFFECT OF ADJUSTING ARMATURE VOLTAGE ON SPEED

## Slide 12
CONTROLLING SPEED BY ADJUSTING ARMATURE VOLTAGE
  THE ONLY CONTROLLED VARIABLE IS THE ARMATURE VOLTAGE OF THE MOTOR, WHICH IS DEPICTED AS AN ADJUSTABLE-VOLTAGE SOURCE.
  •THIS METHOD IS HIGHLY EFFICIENT AND STABLE AND IS SIMPLE TO IMPLEMENT.
  • WHEN THE ARMATURE VOLTAGE IS REDUCED, THE NO-LOAD SPEED Ω_0 IS ALSO REDUCED.
EFFECT OF ADJUSTING ARMATURE VOLTAGE ON SPEED
EXPLANATION

## Slide 13
CONTROLLING SPEED BY ADJUSTING ARMATURE VOLTAGE
  •NOTE THAT WE ARE ASSUMING THE FIELD VOLTAGE IS UNCHANGED WHEN THE ARMATURE VOLTAGE VARIES.
  •ELECTRIC HOLDING CAN BE DONE IF THE ARMATURE VOLTAGE IS REDUCED UNTIL ∆Ω IS EQUAL TO Ω_0.
•MOTOR CHARACTERISTICS WHEN ARMATURE VOLTAGE CHANGES
EXPLANATION

## Slide 14
CONTROLLING SPEED BY ADJUSTING ARMATURE VOLTAGE
•MOTOR CHARACTERISTICS WHEN ARMATURE VOLTAGE CHANGES
EQUATIONS

## Slide 15
The operation
CONTROLLING SPEED BY ADJUSTING FIELD VOLTAGE
Method 1:

## Slide 16
CONTROLLING SPEED BY ADJUSTING FIELD VOLTAGE
A SETUP FOR SPEED CHANGE BY
ADDING ADJUSTING FIELD VOLTAGE
EFFECT OF ADDING ADJUSTING FIELD VOLTAGE ON SPEED

## Slide 17
CONTROLLING SPEED BY ADJUSTING FIELD VOLTAGE
EFFECT OF ADDING ADJUSTING FIELD VOLTAGE ON SPEED
  IF WE REDUCE THE FIELD VOLTAGE, THE FIELD CURRENT AND CONSEQUENTLY THE FLUX ARE REDUCED.
  •EQUATION 2.1 & 2.2 SHOW THE DEPENDENCY OF MOTOR SPEED ON THE FIELD FLUX.
  •THE NO-LOAD SPEED IS INVERSELY PROPORTIONAL TO THE FLUX, AND THE SLOPE OF EQUATION (2.1)IS INVERSELY PROPORTIONAL TO THE SQUARE OF THE FLUX.
EXPLANATION

## Slide 18
CONTROLLING SPEED BY ADJUSTING FIELD VOLTAGE
EFFECT OF ADDING ADJUSTING FIELD VOLTAGE ON SPEED
  WHEN THE FIELD FLUX IS REDUCED, THE NO-LOAD SPEED Ω_0 IS INCREASED IN INVERSE PROPORTION TO THE FLUX, AND THE SPEED DROP ∆Ω IS ALSO INCREASED.
  •WHEN MOTOR SPEED IS CONTROLLED BY ADJUSTING THE FIELD CURRENT, THE FOLLOWING CONSIDERATIONS SHOULD BE KEPT IN MIND.
1. THE FIELD VOLTAGE MUST NOT EXCEED THE ABSOLUTE
MAXIMUM RATING.
2. SINCE DC MOTORS ARE RELATIVELY SENSITIVE TO
VARIATIONS IN FIELD VOLTAGE, LARGE RE-DUCTIONS IN FIELD
CURRENT MAY RESULT IN EXCESSIVE SPEED.
3. BECAUSE THE ARMATURE CURRENT IS INVERSELY
PROPORTIONAL TO THE FIELD FLUX (I_A=T_D/K∅), REDUCING
THE FIELD RESULTS IN AN INCREASE IN THE ARMATURE
CURRENT (ASSUMING THAT THE LOAD TORQUE IS UNCHANGED).
EXPLANATION

## Slide 19
REFLECTIONS
  Solid-state control is used for enhanced efficiency and for versatile operation of electric drive systems.
  For dc machines, converters are often used in the armature circuit to control the terminal voltage of the motor. In some cases, the converter is also used to control the field voltage.

## Slide 20
THANK YOU