## Slide 1: CHAPTER 2: AC TO DC CONVERTER (RECTIFIER)
DET40073:POWER ELECTRONICS

## Slide 2: Course Learning Outcome
Upon completion of this course, students should be able to:
CLO1 : Analyze and investigate the well-defined operational behaviors, principle and basic concepts of Power Electronics by using schematics circuits.
DET40073:POWER ELECTRONICS

## Slide 3: 2.1 Remember the principle operation of Single-Phase AC to DC Converter. 2.2 Apply the principle of Single-Phase AC to DC Converter.
DET40073:POWER ELECTRONICS

## Slide 4: Introduction
A rectifier is an electrical device that converts AC which periodically reverses direction, to DC which flows in only one direction.
The process is called RECTIFICATION.
Input can be single or 3-phase and output can be made fixed or variable.
DET40073:POWER ELECTRONICS

## Slide 5: Classification of AC-DC Converters (Rectifiers)
DET40073:POWER ELECTRONICS
Rectifiers
Three Phase
Single Phase
Uncontrolled
Half Wave
Full Wave
Half Wave
Full Wave
Half Wave
Full Wave
Half Wave
Full Wave
Half Controlled
Half Controlled
Fully Controlled
Fully Controlled
Uncontrolled
Centre-tap
Bridge
Figure 2-1: Classification of AC to DC Converters (Rectifiers)

## Slide 6: Applications
DET40073:POWER ELECTRONICS
DC Motor Drives
DC Welder
DC Power Supply
Battery Charger
HVDC

## Slide 7: Single Phase Uncontrolled Rectifier
THREE types of Single Phase Uncontrolled Rectifier:
DET40073:POWER ELECTRONICS
Half Wave Rectifier
A SINGLE diode is required.
Full Wave Rectifier (Centre-tap)
TWO diodes were used
Full Wave Bridge Rectifier
FOUR diodes were used.
Allows only half cycle (either positive half cycle or negative half cycle) of the input AC signal while the another half cycle is blocked.
DIODES are connected to the centre tapped secondary winding of the transformer.
Centre tap divides the total secondary voltage into equal parts.
This bridge circuit is that it does not require a special center-tapped transformer, thereby reducing its size and cost

## Slide 8: Half Wave Rectifier with Resistive Load
DET40073:POWER ELECTRONICS
Figure 2-2: Half Wave Rectifier with Resistive Load
Figure 2-3: Output Voltage and Current Waveform

## Slide 9: Half Wave Rectifier with Resistive Load
DET40073:POWER ELECTRONICS
Circuit operation:
During positive half cycle:
For interval 0t;
Diode D1 conducts (forward biased).
The input voltage appear across the load.
Vo = Vs
During negative half cycle:
For interval t2;
Diode D1 in blocking condition (reverse biased).
Output voltage is zero.
Vo = 0V.

## Slide 10: Cont. …
DET40073:POWER ELECTRONICS
Derivation for average output voltage:
Figure 2-4: Input and Output Voltage Waveform

## Slide 11: Cont. …
DET40073:POWER ELECTRONICS
Output Voltage and Current:
Where,
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Power factor, pf:

## Slide 12: Half Wave Rectifier with Inductive Load
DET40073:POWER ELECTRONICS
Figure 2-5: Half Wave Rectifier with Inductive Load
Figure 2-6: Output Voltage and Current Waveform

## Slide 13: Cont. …
DET40073:POWER ELECTRONICS
Circuit operation:
During positive half cycle:
For interval 0t;
Diode D1 forward biased.
Vi increase from zero to its positive maximum value and becomes zero again at t=.
For interval t+;
Due to the inductive load, io increases slowly.
D1 continues to conduct till the inductor currents become zero at t=.
Extended angle () due to inductive load.

## Slide 14: Cont. …
DET40073:POWER ELECTRONICS
Circuit operation:
During negative half cycle:
For interval + t2
D1 becomes reverse biased.
Both vo and io remains zero till the beginning of the next cycle.
Both Vo and io is zero.

## Slide 15: Cont. …
DET40073:POWER ELECTRONICS
Derivation for average output voltage:
π+
Figure 2-7: Input and Output Voltage Waveform

## Slide 16: Cont. …
DET40073:POWER ELECTRONICS
Output Voltage and Current:
Where,
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Power factor, pf:

## Slide 17: Half Wave Rectifier R-L Load with Free-Wheeling Diode
DET40073:POWER ELECTRONICS
Figure 2-8: Half Wave Rectifier with Free-Wheeling diode
Figure 2-9: Output Voltage and Current Waveform

## Slide 18: Cont. …
DET40073:POWER ELECTRONICS
Circuit operation:
Diode Dm will prevent negative voltage appearing across the load.
When the supply voltage goes to zero, the current from D1 is transferred across to diode Dm.
This is called commutation of diodes (the charge in the inductor will be used to keep diode Dm on, instead of previously forcing D1 to remain in its forward state).
This would reduce the value of the extended angle of conduction of the diode D1, β to zero.
Output Voltage and Current:
*same as output rectifier with resistive load

## Slide 19: Full Wave Centre-tap Rectifier with Resistive Load
DET40073:POWER ELECTRONICS
Figure 2-10: Full Wave Centre-Tap Rectifier with Resistive Load
Figure 2-11: Output Voltage and Current Waveform

## Slide 20: Cont. …
DET40073:POWER ELECTRONICS
During negative half cycle:
For interval t2;
Diode D2 conducts (D2 forward biased and D1 reverse biased).
Vo=Vs
During positive half cycle:
For interval 0t;
Diode D1 conducts (D1 forward biased and D2 reverse biased).
Vo=Vs
Circuit operation:

## Slide 21: Cont. …
DET40073:POWER ELECTRONICS
Derivation for average output voltage:
Figure 2-12: Input and Output Voltage Waveform

## Slide 22: Cont. …
DET40073:POWER ELECTRONICS
Output Voltage and Current:
Where,
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Power factor, pf:

## Slide 23: Full Wave Bridge Rectifier with Resistive Load
DET40073:POWER ELECTRONICS
Figure 2-13: Full Wave Bridge Rectifier with Resistive Load
Figure 2-14: Output Voltage and Current Waveform

## Slide 24: Cont. …
DET40073:POWER ELECTRONICS
During negative half cycle:
For interval t2;
Diode D3 and D4 conducts
The input voltage appear across the load.
Vo=Vs
During positive half cycle:
For interval 0t;
Diode D1 and D2 conducts
The input voltage appear across the load.
Vo=Vs
Circuit operation:

## Slide 25: Cont. …
DET40073:POWER ELECTRONICS
Derivation for average output voltage:
Figure 2-15: Input and Output Voltage Waveform

## Slide 26: Cont. …
DET40073:POWER ELECTRONICS
Output Voltage and Current:
Where,
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Power factor, pf:

## Slide 27: Full Wave e Rectifier with Highly Inductive Load
DET40073:POWER ELECTRONICS
Figure 2-16: Full Wave Bridge Rectifier with Highly Inductive Load
Figure 2-17: Output Voltage and Current Waveform

## Slide 28
DET40073:POWER ELECTRONICS
Fig. 2.16 presents the circuit connection for a single-phase, full-wave, rectifier loaded with a highly inductive load.
Highly inductive loads are basically R-L loads where L >>> R.
Therefore, the load time constant τ = L/R is very high and can be considered infinity. Consequently, the load current is assumed constant.
For one total period of operation of this circuit, the corresponding waveforms are shown in Fig. 2.17.
During the conduction of D1 and D2 simultaneously the supply voltage appears directly across the load so that the load voltage vo (ωt) remains ( same as the case of resistive load).
Hence, the average value of the load voltage Vdc can be calculated as follows:
Cont. …

## Slide 29
DET40073:POWER ELECTRONICS
Since the load is a highly inductive load. Then, the load current is considered constant (ripple free current) and its average value is;
and the d.c. power is;
The rms value of the load voltage can be calculated as follows:
Therefore the rms value of the load current s is;
The output AC power is given by:
Cont. …

## Slide 30: Example

## Slide 31
DET40073:POWER ELECTRONICS
Example 1:
With reference to Figure-2.18, derive the equation for average output voltage, Given
Solution:
π 2π 3π
Figure-2.18

## Slide 32
DET40073:POWER ELECTRONICS
Example 2:
A single phase half wave uncontrolled rectifier with inductive load is connected from 240Vp, 50Hz source.
Calculate the average output voltage if given the extinction angle =45.
Sketch and label the input and output voltage waveform.
Solution:
Convert from deg to rad.
Calculator mode: rad

## Slide 33
DET40073:POWER ELECTRONICS
Example 3:
A single phase bridge rectifier has a purely resistive load R=10Ω, the supply voltage
, and the supply frequency . Determine the:
  average output voltage
  average output current
  output dc power
Solution:
  average output voltage
  average output current
  output dc power

## Slide 34: POP QUIZ
Referring to Figure-A below, calculate the average output voltage.
Figure A

## Slide 35: Single Phase Controlled Rectifier
THREE types of Single Phase Controlled Rectifier:
  Half Wave Controlled Rectifier
  Full Wave Controlled Centre-Tap Rectifier
  Full Wave Controlled Bridge Rectifier
Controlled Rectifiers are line commutated ac to dc power converters which are used to convert a fixed voltage, fixed frequency ac power supply into variable dc output voltage.
The input supply fed to a is ac supply at a fixed rms voltage and at a fixed frequency.
By employing phase controlled thyristors in the circuits we can obtain variable dc output voltage and variable dc (average) output current by varying the trigger angle (phase angle) at which the thyristors are triggered.
DET40073:POWER ELECTRONICS

## Slide 36: Cont. …
DET40073:POWER ELECTRONICS
A way to control output of a rectifier is to use an SCR instead of a diode.
Two condition must be met before SCR can conduct:
SCR must be forward biased (
SCR must be forward biased (𝑽_𝑺𝑪𝑹>𝟎).
A current must be applied to the gate of SCR.
- The SCR will not begin to conduct as soon as the source becomes positive.
- Conduction is delayed until a gate current is applied.
Once SCR is conducting, the gate current can be removed and the SCR remains ON until the current goes to zero.
A way to control output of a rectifier is to use an SCR instead of a diode.
- The SCR will not begin to conduct as soon as the source becomes positive.
- Conduction is delayed until a gate current is applied.
Once SCR is conducting, the gate current can be removed and the SCR remains ON until the current goes to zero.

## Slide 37
DET40073:POWER ELECTRONICS
Half Wave Controlled Rectifier with Resistive Load
Figure 2-19: Half Wave Controlled Rectifier with Resistive Load
Figure 2-20: Output Voltage and Current Waveform

## Slide 38: Cont. …
DET40073:POWER ELECTRONICS
Circuit operation:
During the positive half cycle, for (0t π):
  The thyristor T1 is forward biased (but not conducting at 0t α)
  When the thyristor is fired at t=α it conducts and the input voltage appears across the load (at αt π).
During the negative half cycle for (π t2π):
  The thyristor is reversed biased and it is turned off.
  Output is zero.
The delay angle α, is defined as the time the input voltage starts to go positive to the time the thyristor is fired.

## Slide 39: Cont. …
DET40073:POWER ELECTRONICS
Derivation for average output voltage:
Figure 2-21: Input and Output Voltage Waveform

## Slide 40: Cont. …
DET40073:POWER ELECTRONICS
Output Voltage and Current:
Where,
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Power factor, pf:

## Slide 41
DET40073:POWER ELECTRONICS
Half Wave Controlled Rectifier with Inductive Load
Figure 2-22: Half Wave Controlled Rectifier with Inductive Load
Figure 2-23: Output Voltage and Current Waveform

## Slide 42: Cont. …
DET40073:POWER ELECTRONICS
Circuit operation:
During the positive half cycle ():
  At , the current through the circuit is zero.
  The SCR is triggered when .
  When , the source becomes zero, but the current through the circuit is not zero and there is some energy stored in the inductor.
During the negative half cycle ():
  The current through the circuit would not become zero suddenly because of the inductor.
  The inductor acts as a source and keeps the SCR forward-biased till the energy stored in the inductor becomes zero.
  The current through the circuit become zero at .
  For , the current through the circuit is zero

## Slide 43: Cont. …
DET40073:POWER ELECTRONICS
Derivation for average output voltage:
Figure 2-24: Input and Output Voltage Waveform

## Slide 44: Cont. …
DET40073:POWER ELECTRONICS
Output Voltage and Current:
Where,
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Power factor, pf:

## Slide 45
DET40073:POWER ELECTRONICS
Half Wave Controlled Centre-Tap Rectifier with Free-Wheeling Diode
Figure 2-25: Half Wave Controlled Rectifier with Free Wheeling Diode
Figure 2-26: Output Voltage and Current Waveform

## Slide 46: Cont. …
DET40073:POWER ELECTRONICS
Function of Free Wheeling Diode:
Diode Dm will prevent negative voltage appearing across the load during negative cycle of input voltage.
When the supply voltage goes to zero at t=, the current from inductor is transferred across diode Dm.
This is called commutation of SCR.
The result is the charge in the inductor will be used to keep diode Dm on, instead of previously forcing SCR to remain in its forward state.
This would reduce the value of the extended angle of conduction of the SCR, β to zero.

## Slide 47: Cont. …
DET40073:POWER ELECTRONICS
Circuit operation:
During the positive half cycle, for interval (0t π):
  At wt =0, the current through the circuit is zero.
  The SCR is triggered when wt=a.
  The input voltage appears across the load
During negative half cycle, for interval (π t 2π):
  The supply voltage goes to zero at t=
  The current from inductor is transferred across diode Dm.
  Output is zero.

## Slide 48: Cont. …
DET40073:POWER ELECTRONICS
Derivation for average output voltage:
Figure 2-27: Input and Output Voltage Waveform
*same as output rectifier with resistive load

## Slide 49
DET40073:POWER ELECTRONICS
Full Wave Controlled Rectifier with Resistive Load
Figure 2-28: Full Wave Controlled Centre-tap Rectifier with Resistive Load
Figure 2-29: Output Voltage and Current Waveform

## Slide 50: Cont. …
DET40073:POWER ELECTRONICS
Circuit operation:
During positive half cycle, for interval (0tπ):
  SCR1 is forward biased.
  When SCR1 is fired at t=α, it conducts and the input voltage appears across the load (at αtπ).
During the negative half cycle, for interval (π t2π):
  SCR2 is forward biased.
  When SCR2 is fired at t=π+α and it conduct until 2π.
  The input voltage appears across the load(at π+αt2π).

## Slide 51: Cont. …
DET40073:POWER ELECTRONICS
Figure 2-30: Input and Output Voltage Waveform
Derivation for average output voltage:

## Slide 52: Cont. …
DET40073:POWER ELECTRONICS
Output Voltage and Current:
Where,
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Power factor, pf:

## Slide 53
DET40073:POWER ELECTRONICS
Full Wave Controlled Centre-Tap Rectifier with Highly Inductive Load
Figure 2-31: Full Wave Controlled Centre-tap Rectifier with Inductive Load
Figure 2-32: Output Voltage and Current Waveform

## Slide 54: Cont. …
DET40073:POWER ELECTRONICS
Highly inductive load, L>>R:
The high-load inductance generates a perfectly filtered current and the rectifier behaves like a current source.
Referring to Figure 2-31, can be fired into the on-state at any time after goes positive. One is turned-on, current builds up in the inductive load, maintaining in the on-state up to the period when goes negative. Once goes negative, becomes positive, and the firing immediately turns on thyristor which takes up the load current, placing reverse voltage on , its current being commutated (transferred) to .
The load current can be continuous or discontinuous depending on the inductance value.

## Slide 55: Cont. …
DET40073:POWER ELECTRONICS
Circuit operation:
During positive half cycle, for interval (0tπ):
  SCR1 is forward biased and conduct when t=α.
  Due to inductive load, SCR1 continue to conduct beyond t=.
During the negative half cycle, for interval (π t2π):
  SCR2 is forward biased and conducts at t=π+α.
  SCR1 continue to conduct beyond t=2.

## Slide 56: Cont. …
DET40073:POWER ELECTRONICS
@
Derivation of average output voltage:
Figure 2-33: Input and Output Voltage Waveform

## Slide 57: Cont. …
DET40073:POWER ELECTRONICS
Output Voltage and Current:
Where,
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Power factor, pf:

## Slide 58
DET40073:POWER ELECTRONICS
Full Wave Controlled Centre-Tap Rectifier with Free-Wheeling Diode
Figure 2-34: Full Wave Controlled Centre-tap Rectifier with Free Wheeling Diode
Figure 2-35: Output Voltage and Current Waveform

## Slide 59: Cont. …
DET40073:POWER ELECTRONICS
Figure 2-36: Input and Output Voltage Waveform
Derivation of average output voltage:
*same as output rectifier with resistive load

## Slide 60
DET40073:POWER ELECTRONICS
Full Wave Controlled Bridge Rectifier with Resistive Load
Figure 2-37: Full Wave Controlled Bridge Rectifier with Resistive Load
Figure 2-38: Output Voltage and Current Waveform

## Slide 61: Cont. …
DET40073:POWER ELECTRONICS
Circuit operation:
During positive half cycle, for interval (0tπ):
  SCR1 and SCR4 forward biased.
  When SCR1 and SCR4 is fired at t=α, it conducts and the input voltage appears across the load(at αtπ).
During the negative half cycle, for interval (π t2π):
  SCR2 and SCR3 is forward biased.
  When SCR2 and SCR3 is fired at t=π+α and it conduct until 2π.
  The input voltage appears across the load(at π+αt2π).

## Slide 62: Cont. …
DET40073:POWER ELECTRONICS
Figure 2-39: Input and Output Voltage Waveform
*note that the derivation for output voltage for full wave centre-tap and full wave bridge rectifier is same because both rectifier generates the same output waveform.
Derivation of average output voltage:

## Slide 63: Cont. …
DET40073:POWER ELECTRONICS
Output Voltage and Current:
Where,
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Power factor, pf:

## Slide 64
DET40073:POWER ELECTRONICS
Full Wave Controlled Bridge Rectifier with Inductive Load
Figure 2-40: Full Wave Controlled Bridge Rectifier with Resistive Load
Figure 2-41: Output Voltage and Current Waveform

## Slide 65: Cont. …
DET40073:POWER ELECTRONICS
Circuit operation:
During positive half cycle, for interval ():
  SCR1 and SCR4 is triggered when .
  When , the source becomes zero, but the current through the circuit is not zero and there is some energy stored in the inductor.
  It and keeps the SCR1 and SCR4 forward-biased till the energy stored in the inductor becomes zero at .
During the negative half cycle, for interval ():
  SCR2 and SCR3 is triggered when
  When , the source becomes zero, but the current through the circuit is not zero and there is some energy stored in the inductor.
  It and keeps the SCR2 and SCR3 forward-biased till the energy stored in the inductor becomes zero at .

## Slide 66: Cont. …
DET40073:POWER ELECTRONICS
Figure 2-42: Input and Output Voltage Waveform
Derivation of average output voltage:

## Slide 67: Cont. …
DET40073:POWER ELECTRONICS
Output Voltage and Current:
Where,
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Parameters | DC components | Rms values
Output voltage |  | 
Output current |  | 
Output power |  | 
Power factor, pf:

## Slide 68: Example

## Slide 69
DET40073:POWER ELECTRONICS
Example 4:
Solution:
  Based on Figure 2-44 below:
  Explain the operation for interval .
  Calculate the average output voltage and current if the peak voltage is 115V and the resistive load R=25Ω.
Circuit operation:
  During interval:
    The SCR is triggered when .
    When , the source becomes zero, but the current through the circuit is not zero and there is some energy stored in the inductor.
    The inductor acts as a source and keeps the SCR forward-biased till the energy stored in the inductor becomes zero.
    The current through the circuit become zero at .
    average output voltage and current:
Figure 2-44

## Slide 70
DET40073:POWER ELECTRONICS
Example 5:
A full wave centre-tap rectifier has an ac input of 120 at 50Hz, and a 20Ω load resistor. The delay angle is . Determine the dc output current and power.
Solution:
  Dc output current:
  Dc output power:

## Slide 71
DET40073:POWER ELECTRONICS
Example 6:
A controlled full wave bridge rectifier has a source of 120 at 60Hz, R=10Ω, L=10mH, and and . Determine:
  An expression of average output voltage
  Average output voltage and current.
  Sketch the output voltage and current.
Solution:
  An expression of average output voltage:

## Slide 72: Cont. …
DET40073:POWER ELECTRONICS
  Average output voltage and current.
  Sketch the output voltage and current.

## Slide 73: 2.3 Investigate the principle operation of Single Phase Half Wave Ac to Dc Converter: 2.3.1 Analyze effects of inductive load 2.3.2 Investigate method used to overcome the effects appeared due to existence of inductance loads.
DET40073:POWER ELECTRONICS

## Slide 74: Cont. …
DET40073:POWER ELECTRONICS
The effect of load inductance:
Due to the presence of load inductance the output voltage reverses and becomes negative.
This reduces the dc output voltage.
Method used to overcome:
To prevent this reduction of dc output voltage due to the negative region in the output load voltage waveform, a free wheeling diode is connected across the load.
The output voltage waveform and the dc output voltage obtained would be the same as that for a rectifier with resistive load.

## Slide 75: 2.4 Investigate the principle operation of Single Phase Half Wave Ac to Dc Converter: 2.4.1 Analyze the differences of continuous and discontinuous output current.
DET40073:POWER ELECTRONICS

## Slide 76: Cont. …
DET40073:POWER ELECTRONICS
Continuous current:
RL load of continuous current is shown in Figure 2-43(a).
In continuous current, the current at must be greater than zero for continuous current operation.
Case of RL load with large R/L ratio.
]
Figure 2-43(a): Continuous current for RL load
Figure 2-43(b): Discontinuous current for RL load
Discontinuous current:
RL load of discontinuous current is shown in Figure 2-43(b).
The current remains at zero at .
Case of RL load with small R/L ratio.

## Slide 77: 2.5 Apply the principle operation of three phase half wave AC to DC Converter.
DET40073:POWER ELECTRONICS

## Slide 78: Three Phase Uncontrolled Rectifier
DET40073:POWER ELECTRONICS
Three-phase diode rectifier circuits are used widely in high power applications with low output ripple.
Operate from 3 phase ac supply voltage
They provide higher dc output voltage and higher dc output power.
Higher output voltage ripple frequency
Extensively used in high power variable speed industrial dc drives.

## Slide 79: Cont. …
DET40073:POWER ELECTRONICS
Figure 2-45: 3-phase Waveform
Figure 2-46: 3-phase Supply Voltage

## Slide 80
DET40073:POWER ELECTRONICS
Three Phase Half Wave Rectifier
Using THREE diodes/SCRs.
Three-phase diode rectifier circuits are used widely in high power applications with low output ripple.
The advantage here is that 3-phase rectification circuits can be used to power many industrial applications such as motor control or battery charging which require higher power requirements than a single-phase rectifier circuit is able to supply.

## Slide 81
DET40073:POWER ELECTRONICS
3- Half Wave Uncontrolled Rectifier with Resistive Load
Figure 2-47: Half Wave Rectifier with Resistive Load
Figure 2-48: Output Voltage
Waveform

## Slide 82: Cont. …
DET40073:POWER ELECTRONICS
Circuit operation:
While V1 is the most positive phase, diode D1 conduct but directly V2 become more positive than V1, the load current commutates(transfers) from diode D1 to diode D2
Once V3 is more positive than V2 the load current commutates (transfers) from diode D2 to diode D3 and the process is repeat on the next cycle.

## Slide 83: Cont. …
DET40073:POWER ELECTRONICS
Period | On diode | Off diodes | Output Phase Voltage
0 - 30° |  | & | 
30°- 150° |  | & | 
150°- 270° |  | & | 
270°- 390° |  | & | 
Period | On diode | Off diodes | Output Phase Voltage
0 - 30° |  |  | 
30°- 150° |  |  | 
150°- 270° |  |  | 
270°- 390° |  |  | 
Output waveform:

## Slide 84: Cont. …
DET40073:POWER ELECTRONICS
Output Voltage
and Current

## Slide 85
DET40073:POWER ELECTRONICS
3- Half Wave Controlled Rectifier with Resistive Load
Figure 2-49: Half Wave Controlled Rectifier with Resistive Load
Figure 2-50: Output Voltage Waveform

## Slide 86: Cont. …
DET40073:POWER ELECTRONICS
Circuit operation:
T1is triggered at and the phase voltage appears across the load until T2 is fired.
T2 is triggered at , T1 becomes reverse biased and the phase voltage appears across the load until T3 is fired.
T3 is triggered at , T2 becomes reverse biased and the phase voltage appears across the load until T1 is fired for the next input cycle.

## Slide 87: Cont. …
DET40073:POWER ELECTRONICS
Output Voltage
and Current
V
For α > 30 :
For α < 30 :

## Slide 88
DET40073:POWER ELECTRONICS
3- Half Wave Controlled Rectifier (R Load) with Different Triggering Angle, .
Figure 2-51: Output Voltage Waveform with Different Triggering Angle, .

## Slide 90
THREE PHASE HALF WAVE CONTROLLED RECTIFIER
WITH R-L LOAD
VA VB VC
Vin
0°
120°
240°
VA
VB
VC
Vo, RL load
α
α
α
β
β
β
Va = 30° + α Vb = 150° + α Vc = 270° + α

## Slide 91: THREE PHASE HALF WAVE CONTROLLED RECTIFIER WITH R-L LOAD
Output Voltage Waveform for Different Trigger Angles

## Slide 92: Example

## Slide 93
Input Voltage Waveform
Output Voltage /Load Voltage Waveform
DET40073:POWER ELECTRONICS
Example 7:
Solution:
Referring to Figure 2-52. Sketch:
Input voltage waveform for each phase.
Voltage waveform of the load.
Figure 2-52

## Slide 94
Output Voltage Waveform
Average output voltage
DET40073:POWER ELECTRONICS
Example 8:
Solution:
Referring to figure 2.53, answer the following questions:
Sketch and label the input voltage, Vin an output voltage, Vout if the firing angle, =30.
If the input voltage, Vin=132sint, with the firing angle =30 and resistive loadR=1k, calculate the average output voltage, Vo,avg.
Figure 2-53

## Slide 95: THREE PHASE FULL WAVE UNCONTROLLED RECTIFIER WITH R LOAD
𝟑 𝟑
𝑽𝒐 = 𝝅 𝑽𝒎
VA
VB
VC
Vo
Vin
VA VB VC
VAB
VAC
VBC
VBA VCA VCB

## Slide 96: THREE PHASE FULL WAVE UNCONTROLLED RECTIFIER WITH R LOAD

## Slide 97
THREE PHASE FULL WAVE UNCONTROLLED RECTIFIER
WITH R LOAD
Vo
Full wave uncontrolled with R load
Vin Va
Vb
Vc

## Slide 98
THREE PHASE FULL WAVE UNCONTROLLED RECTIFIER
WITH R LOAD

## Slide 99: THREE PHASE FULL WAVE UNCONTROLLED RECTIFIER WITH R LOAD
Vo
Vin
VA VB VC
VAB
VAC
VBC
VBA VCA VCB

## Slide 100
𝟑 𝟑
𝑽𝒐 = 𝝅 𝑽𝒎 𝐜𝐨𝐬 𝛉
VA
VB
VC
Vo
VAB
VAC
VBC
VBA VCA VCB
THREE PHASE FULL WAVE CONTROLLED RECTIFIER
WITH R LOAD
Vin
VA VB VC

## Slide 101
Vo
THREE PHASE FULL WAVE CONTROLLED RECTIFIER
WITH R LOAD
Vin
Full wave controlled with R load α = 15°

## Slide 102
THREE PHASE FULL WAVE CONTROLLED RECTIFIER
WITH R LOAD
Full wave controlled with R load α = 45°
Full wave controlled with R load α = 30°
Full wave controlled with R load α = 60°

## Slide 103: 2.6 Compare the advantages and disadvantages of three-phase over single phase AC to DC Converter.

## Slide 104
DET40073:POWER ELECTRONICS
Cont. …
Figure 2-53: 1 and 3 Supply System
Advantages of 3 Rectifiers over 1 Rectifiers:
Higher output voltage.
Lower amplitude ripples i.e, ouput voltage is smoother.
Higher frequency ripples, simplifying filtering.
Higher overall efficiency.
Disadvantages of 3 Rectifiers over 1 Rectifiers:
High in cost.
It requires a 4-wire supply.

## Slide 105
DET40073:POWER ELECTRONICS
SUCCESS IS NO ACCIDENT. IT IS A HARD WORK, PERSEVERANCE, LEARNING, STUDYING, SACRIFICE AND MOST OF ALL, LOVE OF WHAT YOU ARE DOING.

## Slide 106: Thank you!